Daily Inspection & Flight Notes

Faulke 26	YHB

These are notes to prompt your extra attention during the course of your normal DI

Unattended Canopy – Keep it Closed

Walk Around Inspection

Front Fuselage

Check all surfaces – Fasteners on Engine Cover Secure Fuselage and around main landing gear.

Landing Gear Struts for Security & Cracking

Tyre condition & inflation pressure main wheel

Left Wing

Upper & lower surfaces for damage

Aileron secure and operating freely

Rear Fuselage

Fuselage and vertical stabilizer for damage

Fuselage around tail wheel for damage

Tail wheel condition & inflation pressure

Horizontal Stabilizer

Door closed & taped

Elevator secure & operating freely

No Damage

Rudder

Condition, secure & operating freely

Right Wing

Upper & lower surfaces for damage

Aileron secure and operating freely

Daily Inspection – Continued Section 2

These are notes to prompt your extra attention during the course of your normal DI

Walk Around Inspection

Engine - Visually Check

Break Assembly

All Screw, Bolts & Fasteners

Rubber Engine Mounts

Muffler Assembly

Fuel Lines, Harnesses

Ignition Cables & Sparkplug Caps

Carb, Filters, Lines & Cable Controls

Engine Compartment Clean & Clear

Engine Bay Door Covers (hinges and cracking)

Engine Hold Down Assembly

Propeller

Prop Tip Play (< = 6mm) (2* radial)

Leading Edge for Damage

Prop Main Bearing Tightness

Fuselage Fuel Tank

Drain Fuel Sample

Check Fuel Level

Fuel Cap Secure

Daily Inspection – Continued Section 3

Pre-Flight Cockpit Check

- Ignition Off

- Priority Switch to Appropriate Seat

(FRONT or REAR COMMAND)

- Side Circuit Breakers:  CHECK

- Front Panel Circuit Breakers:  CHECK

- Master: ON

- Engine Electrics: ON

- Check Voltage: Need > 11.9 volts

- Reserve Battery Check: GREEN LIGHT

- Fuel Qty on Gauge matches physical check

- Fuel Transfer Selector

CHECK Fuel Transfer Light ON

- Avionics: ON

- Intercom: ON

- Radio: CHECK – Set Local or Required Frequency

- Set Field Elevation QNH – Electric Vario	?????????

- Altimeter: SET QNH Local

- Front & Rear PTT: CHECK

- Headsets: CHECK Intercom

- Flarm; ON

Pre COCKPIT ENTRY

  - Controls – Correct Sense – Free Movement

Engine GROUND START

- CHECK  Priority Switch

(FRONT or REAR COMMAND)

2.	Master: ON

3.	Avionics: ON

4.	Engine Electrics: ON

5.	Power Plant “T” Handle Pull

(only if power plant not up)

6.	Extend Engine Light: ON

(Visual Confirmation of Powerplant Extention)

7.	Propeller Take-Off Light: ON

8.	Fuel Valve: OPEN – Full Forward

9.	Throttle: CLOSED

10.	Choke: OFF

11.	APPLY WHEEL BREAK

12.	Ignition: START (If no initial ignition,

Engage for 10 seconds @ 10 second intervals)

- Generator: CHECK for > 13v

- Soaring Master: ON

Pre-Flight – C.H.A.O.T.I.C

Controls		Free & Correct in Each Sence

Harnesses		Fastened Correctly

Airbreaks 		Open – Closed & Locked

Outside		Weather / Wind & Runway Selection

Trim   			SET 1/3 Nose UP

Instaments		All Operational & SET CORRECTLY

Canopy Locked   – 	Controls Free

Engine Run Up – Pre Take Off

1.	Prop Take Off Light: ON

2.	Mag CHECKS

3.	APPLY WHEEL BREAK

4.	Throttle Open to 6200—6400 rpm

5.	Check Each Mag approx <100 rpm drop

6.	Throttle Idle: SET Ignition Switch to BOTH

7.	OK to Take Off at CHT 120 C ??????

Final CHECKS  &  TAKE OFF

Four “F’s”  -  Five “C’s”  -  Two “T’s”

- Fuel:   ON

- Fuel:   SUFFICIENT

- Frequency Radio:   CORRECT

- Flaps:   SET

- Choke:   OFF

- Carby Heat:   OFF             ????

- Cowl Flap:   CLOSED

- Canopy;   LOCKED

- Circuit:   CLEAR

- Trim  -  CHECK

- Time  -  CHECK

TAKE OFF

- Hold Wheel Break ON

- Throttle Full Open   -----  MAX rpm 6800

- Release Wheel Break –

Put Away Airbrakes & LOCK

- Maintain Nose Wheel Contact until 30 kts

Vr	 40 – 43 kts

- Takeoff and Climb 55 kts

(Increase Angle of Attack to Control Over Revving)

- EGT: Equal Readings

- CHT: 180 C Max	???????

INFLIGHT – STOP –

& ENGINE RETRACTION

- Throttle Back to 5000 rpm

(Cool to CHT 155 C at 50 kts)

- At CHT 155 C : Close Throttle - Idle

- Speed 48 – 50 kts

- Set Trim for 48 – 50 kts

- When CHT is 140 – 145 C Ignition:  OFF

(ALL the WAY)

- Propeller Break – APPLY SMOOTHLY

STOP Propeller CENTRED VERTICAL

“HOLD BREAK ON UNTIL POWER UNIT 
			IS AWAY COMPLETELY”

- Stored Power Plant away

(VISUAL CHECK – in Mirror & listen for “clunk”)

- Static Source; Soaring Flight:   ON

- Fuel Cock:	OFF

- Master:	OFF

- Head Sets	OFF

INFLIGHT - ENGINE EXTENTION - & START

1.	Master:   ON

2.	Switch to Head Sets;	ON  -  Put Head Sets:	ON

3.	Trim for 48 kts

4.	Engine Electrics:   ON

5.	Start Engine

6.	Fuel Cock:   ON

7.	HOLD PROPELLER BREAK

Until Power Plant is FULLY EXTENDED

8.	Pull “T” Handle to Extend Power Plant

9.	Power Plant Extension Light:   ON

10.	Check Power Plant (VISUALLY) for full Extension

11.	Ignition:  START then BOTH

12.	Engine Warm Up to 1500 RPM

then FULL POWER

13.	Static Source:   POWER FLIGHT

14.	Avionics:   ON	???????????

GLIDER Pre LANDING

- Flaps	Not Fitted

- Under Carriage	Fixed

- Speed Landing	58 kts

+5 kts every 10 kts of

wind speed

- Set Trim for	As above kts

- Airbrakes	Test Leave Unlocked

X-Wind component 16 kts

POWERED Pre LANDING

Same as Glide Configuration

PLUS

- Throttle	Closed at

End of Down Wind

END of FLIGHT/DAY

- All Switches:  OFF

- Record all Details in Flight Book

- Clean Leading Edges

- Put Battery on Charge

- Close Canopy

- Put Cover on Canopy

Packing for Cross Country

- H2O – Anti Dehydration Fluid	-Water

- Food Stores

- Parachutes

- Sanitation Equipment: Bags, Towels, etc

- Maps and Notes

- Sunglasses

- Sunscreen

- Hat and Clothing

- Calculator

- GPS // FLARM

- Engine Oil

Radio Frequencies		Call Signs

| Tyagarah | 126.7 |  | Jump Plane | ZMV |
| --- | --- | --- | --- | --- |
| Lismore | 124.2 |  | Domona | ZDD |
| Murwillumba | 126.7 |  | Falke | YHB |
| Casino | 126.2 |  | " | XJX |
| Gold Coast Tower | 118.7 |  | " |  |
| Ballina | 124.2 |  | Ashley | PIK |
| Warwick | 12 |  | Russell 109 | FFN |
| Evans Head | 124.2 |  | DG505 | K |
| Johndaryan |  |  | ASK21 | JBW |
| Boonah | 122.75 |  | Faulk Blue | GLA |
| Local Chat | 122.7 |  | " Yel | GVZ |
| Karalbyn | 126.65 |  |  |  |
| Area West | 130.4 |  |  |  |
| Brisbane Radar | 119.5 |  |  |  |