Daily Inspection & Flight Notes

GROB 103 S/L	GLL

These are notes to prompt your extra attention during the course of your normal DI

Unattended Canopy – Keep it Closed

Walk Around Inspection

Front Fuselage

Check all surfaces for buckling, cracking and unevenness, especially around lower surface of fuselage and around main landing gear.

Pitot tube open

Nose wheel area of fuselage for damage

Tyre condition & inflation pressure both nose & main wheel

Wheel pants secure

Left Wing

Upper & lower surfaces for damage

Wing wheel

Aileron secure and operating freely

Tape joint seal in place

Rear Fuselage

Fuselage and vertical stabilizer for damage

Fuselage around tail wheel for damage

Tail wheel condition & inflation pressure

Static ports and TEK Probe open

Horizontal Stabilizer

Correct assembly:  Door closed & taped

Elevator secure & operating freely

Tape joint seal in place

Rudder

Condition, secure & operating freely

Tape joint seal in place

Right Wing

Upper & lower surfaces for damage

Wing wheel

Aileron secure and operating freely

Tape joint seal in place

Daily Inspection – Continued Section 2

These are notes to prompt your extra attention during the course of your normal DI

Walk Around Inspection

Extended Engine - Visually Check

Break Assembly

Prop Centring Assembly

Prop Pitch Changing Assembly

All Screw, Bolts & Fasteners

Rubber Engine Mounts

Arrestor Cables

Muffler Assembly

Routing of all Cables, Fuel Lines, Harnesses

Tooth Belt Condition & Tension

Ignition Cables & Sparkplug Caps

Engine Cover Plates (secure) - right hand critical

Carb, Filters, Lines & Cable Controls

Engine Compartment Clean & Clear

Engine Bay Door Covers (hinges and cracking)

Engine Hold Down Assembly

Propeller

Prop Tip Play (< = 6mm) (2* radial)

Leading Edge for Damage

Prop Main Bearing Tightness

Fuselage Fuel Tank

Drain Fuel Sample

Check Fuel Level

Fuel Cap & Cover Secure

Wing Tank

Tilt Plane on Left Wing – Take Fuel Sample

Check Fuel Level

Secure Fuel Cap

Weight and Balance

CHECK - Cockpit, Tail, & Fin BALAST

Daily Inspection – Continued Section 3

Pre-Flight Cockpit Check

- Ignition Off

- Priority Switch to Appropriate Seat

(FRONT or REAR COMMAND)

- Side Circuit Breakers:  CHECK

- Front Panel Circuit Breakers:  CHECK

- Master: ON

- Engine Electrics: ON

- Check Voltage: Need > 11.9 volts

- Reserve Battery Check: GREEN LIGHT

- Fuel Qty on Gauge matches physical check

- Fuel Transfer Selector

CHECK Fuel Transfer Light ON

- Avionics: ON

- Intercom: ON

- Radio: CHECK – Set Local or Required Frequency

- Set Field Elevation QNH – Electric Vario	?????????

- Altimeter: SET QNH Local

- Front & Rear PTT: CHECK

- Headsets: CHECK Intercom

- Avionics: OFF

- Soaring Master: OFF

Pre COCKPIT ENTRY

  - Weight and Balast  ( Solo or Dual )

CONFIRM, Cockpit,  Tail,  &  Fin  BALAST CORRECT

  - Dolly & Wing Walker – OFF

  - Controls – Correct Sense – Free Movement

Engine GROUND START

- CHECK  Priority Switch

(FRONT or REAR COMMAND)

2.	Master: ON

3.	Avionics: ON

4.	Engine Electrics: ON

5.	Power Plant “T” Handle Pull

(only if power plant not up)

6.	Extend Engine Light: ON

(Visual Confirmation of Powerplant Extention)

7.	Propeller Take-Off Light: ON

8.	Fuel Valve: OPEN – Full Forward

9.	Throttle: CLOSED

10.	Choke: OFF

11.	APPLY WHEEL BREAK

12.	Ignition: START (If no initial ignition,

Engage for 10 seconds @ 10 second intervals)

- Generator: CHECK for > 13v

- Soaring Master: ON

Pre-Flight – C.H.A.O.T.I.C

Controls		Free & Correct in Each Sence

Harnesses		Fastened Correctly

Airbreaks 		Open – Closed & Locked

Outside		Weather / Wind & Runway Selection

Trim   			SET 1/3 Nose UP

Instaments		All Operational & SET CORRECTLY

Canopy Locked   – 	Controls Free

Engine Run Up – Pre Take Off

1.	Prop Take Off Light: ON

2.	Mag CHECKS

3.	APPLY WHEEL BREAK

4.	Throttle Open to 6200—6400 rpm

5.	Check Each Mag approx <100 rpm drop

6.	Throttle Idle: SET Ignition Switch to BOTH

7.	OK to Take Off at CHT 120 C ??????

Final CHECKS  &  TAKE OFF

Five “F’s”  -  Five “C’s”  -  Two “T’s”

- Fuel:   ON

- Fuel:   SUFFICIENT

- Fuel Pump on (circuit breaker)

- Frequency Radio:   CORRECT

- Flaps:   SET

- Choke:   OFF

- Carby Heat:   OFF             ????

- Cowl Flap:   CLOSED

- Canopy;   LOCKED

- Circuit:   CLEAR

- Trim  -  CHECK

- Time  -  CHECK

TAKE OFF

- Hold Wheel Break ON

- Throttle Full Open   -----  MAX rpm 6800

- Release Wheel Break –

Put Away Airbrakes & LOCK

- Maintain Nose Wheel Contact until 30 kts

Vr	 40 – 43 kts

- Climb Less than Blue Line

(Increase Angle of Attack to Control Over Revving)

(Max rpm 6800)

- EGT: Equal Readings

- CHT: 180 C Max	???????

INFLIGHT – STOP –

& ENGINE RETRACTION

- Throttle Back to 5000 rpm

(Cool to CHT 155 C at 50 kts)

- At CHT 155 C : Close Throttle - Idle

- Speed 48 – 50 kts

- Set Trim for 48 – 50 kts

- When CHT is 140 – 145 C Ignition:  OFF

(ALL the WAY)

- Propeller Break – APPLY SMOOTHLY

STOP Propeller CENTRED VERTICAL

“HOLD BREAK ON UNTIL POWER UNIT 
			IS AWAY COMPLETELY”

- Stored Power Plant away

(VISUAL CHECK – in Mirror & listen for “clunk”)

- Static Source; Soaring Flight:   ON

- Fuel Cock:	OFF

- Master:	OFF

- Head Sets	OFF

INFLIGHT - ENGINE EXTENTION - & START

1.	Master:   ON

2.	Switch to Head Sets;	ON  -  Put Head Sets:	ON

3.	Trim for 48 kts

4.	Engine Electrics:   ON

5.	Propeller Set:   TAKE OFF

6.	Fuel Cock:   ON

7.	HOLD PROPELLER BREAK

Until Power Plant is FULLY EXTENDED

8.	Pull “T” Handle to Extend Power Plant

9.	Power Plant Extension Light:   ON

10.	Check Power Plant (VISUALLY) for full Extension

11.	Ignition:  START then BOTH

12.	Engine Warm Up to CHT 120 C

then FULL POWER

13.	Static Source:   POWER FLIGHT

14.	Avionics:   ON	???????????

GLIDER Pre LANDING

- Flaps	Not Fitted

- Under Carriage	Fixed

- Speed Landing	58 kts

+5 kts every 10 kts of

wind speed

- Set Trim for	As above kts

- Airbrakes	Test Leave Unlocked

X-Wind component 16 kts

POWERED Pre LANDING

Same as Glide Configuration

PLUS

- Propeller	Takeoff Position

- Throttle	Closed at

End of Down Wind

END of FLIGHT/DAY

- All Switches:  OFF

- Record all Details in Flight Book

- Clean Leading Edges

- Put Battery on Charge

- Close Canopy

- Put Cover on Canopy

Packing for Cross Country

- H2O – Anti Dehydration Fluid	-Water

- Food Stores

- Parachutes

- Sanitation Equipment: Bags, Towels, etc

- Maps and Notes

- Sunglasses

- Sunscreen

- Hat and Clothing

- Calculator

- GPS // FLARM

- Two Stroke Engine Oil

- Weight and Balance

Radio Frequencies		Call Signs

| Tyagarah | 126.7 |  | Jump Plane | ZMV |
| --- | --- | --- | --- | --- |
| Lismore | 124.2 |  | Domona | ZDD |
| Murwillumba | 126.7 |  | Falke | YHB |
| Casino | 126.2 |  | " | XJX |
| Gold Coast Tower | 118.7 |  | " |  |
| Ballina | 124.2 |  | Ashley | PIK |
| Warwick | 12 |  | Russell 109 | FFN |
| Evans Head | 124.2 |  | DG505 | K |
| Johndaryan |  |  | ASK21 | JBW |
| Boonah | 122.75 |  | Faulk Blue | GLA |
| Local Chat | 122.7 |  | " Yel | GVZ |
| Karalbyn | 126.65 |  |  |  |
| Area West | 130.4 |  |  |  |
| Brisbane Radar | 119.5 |  |  |  |