TAKE-OFF DISTANCE S2500 fitted to Dimona h36

All figures are based on ICAO std atmosphere, Gross Weight of 770kg

Airfield conditions: calm, dry flat surface with short grass.

Take off speed	45kts (83km/h)

Climb speed (min)	46kts (85km/h)

Field			Outside air temp

Elevation	-15degC	0degC		15degC	30degC

Take-off roll		0 m 		168		180		191		203

until lift off		250(820ft)	174		187		198		210

500(1640ft)	180		193		205		217

750(2461ft)	187		200		212		227

1000(3281ft)	193		207		222		243

Field			Outside air temp

Elevation	-15degC	0degC		15degC	30degC

Take-off 		0 m 		346		364		382		401

distance to		250(820ft)	355		373		392		410

clear 15m-		500(1640ft)	364		382		404		423

50ft obstacle		750(2461ft)	373		395		414		436

1000(3281ft)	385		404		426		446

ATTENTION

The submitted takeoff apply for a paved runway (asphalt) For other surfaces, the surcharges in accordance AIP 1

Terrain flat, dry ,short grass additional	20%

Wet grass  additional 				10%

Softened water logged surface additional 	50%

High grass vegetation additional 		20%

Slush and standing water additional 		30%

Sea level, temperature +15 deg C

Best climb rate propellor in fine (climb): 3.4m / s

Flying speed "best climbing" 52kts (95km/h)

For a set maximum speed of 2900rpm is a maximum horizontal flight speed of 100kts (180-190 km/h) IAS.  The condition of the engine and the aircraft must be impeccable. Wings and propeller must be free of dirt and insects. Be advised Sauer engine manual requires use of maximum power for MAX 5 min then for sustained use max engine speed is 2700rpm and CHT must be monitored continually during use of high engine power.

Range:

At a cruise speed of 95kts (170 km/h) and propeller near revs at 2700rpm on a cruise at 5000ft  the range is about 810km with no reserve and wind factor not considered. The statement applies for a  of 80 lit tank.